Private Pilot Navigation – Homework Assignment

Cross-Country Route

The cross-country is a day VFR flight from the Sudbury airport (CYSB, N46°37’ W80°47’) to the Kitchener airport (CYKF, N43°27’ W80°22’) via the Orillia airport (CNJ4, N44°41’ W79°19’).

You depart the Sudbury airport at 1700 UTC and set course overhead direct to the Orillia airport with a planned 45 min stop at the Orillia airport. Depart the Orillia airport and set course overhead direct to the Kitchener airport.

Winds at all altitudes 	095°T at 18 kt

True Airspeed	130 kt

Fuel Burn	7.2 gal/hr

Each take-off, departure and climb-out 	8 mins / 12 NM / 4.9 gals

CAS = IAS

Required Materials

- Attached weather package

  - TAFs and METARs

  - FDs

- Navigation log

Questions

Flight Planning

- What is the distance between the following two geographic co-ordinates: N49°05’ W82°12’ and N50°05’ W82°12’?

- What is the edition number and publication date for your VNC?

- What is the highest elevation on the Toronto VNC?

- What the total distance flown for the entire trip?

- What is your ETA to Kitchener?

  - Local:

  - UTC:

- Which cruising altitude would be most appropriate for the 1st leg from Sudbury to Orillia?

  - 4500’ ASL

  - 4500’ AGL

  - 5500’ ASL

  - 5500’ AGL

- Once leveling off at the altitude indicated in question 6, what is your calibrated airspeed?

- Can you refuel in Orillia; if so what type of fuel is available?

- Select the correct statements with respect to the Orillia’s aerodrome information.

    - Circuits are right hand on runways 04 and 12

    - Aircraft radio controlled aerodrome light is available

    - There are PAPI lights on runways 12 and 30

    - Customs service is available

    - There is an FSS at the aerodrome

    - Aviation gasoline is available

- What is the Day VFR fuel requirement for the:

  - First leg ________gallons

  - Second leg __________gallons

  - Whole trip__________gallons

- 40 minutes after your set heading over the Sudbury airport you find yourself over the town of Dunchurch. N45°38’30” W79°51’20”. Using opening and closing angles what is your new magnetic heading to Orillia?

- Using the information in question 11 what is your new ETA to Orillia?

- While joining the circuit at Orillia, what class of airspace are you in?

- Which cruising altitude would be most appropriate for the 2nd leg from Orillia to Kitchener?

  - 4500 ASL

  - 4500 AGL

  - 5500 ASL

  - 5500 AGL

- With the VOR receiver tuned to the Toronto VOR (N43°40’ W79°38’), when you are over the town of Everton (N43°40’ W80°10’) the CDI should be

  - Deflected full left with a “From” indication when the OBS is 305°

  - Deflected full left with a “From” indication when the OBS is 125°

  - Deflected full right with a “To” indication when the OBS is 125°

  - Deflected full right with a “From” indication when the OBS is 305°

- What is the frequency and morse code for the Toronto VOR?

Bonus Question

- Using the cruising altitude from question 14 what is the expected reception distance in nautical miles for the Toronto VOR?

## Appendix

## SUDBURY/ON

METAR CYSB 251600Z 17016KT 20SM SCT038 BKN180 02/M00 A3041 RMK SC4CI3 
SLP315=

METAR CYSB 251500Z 16014KT 20SM BKN038 01/M01 A3042 RMK SC6 SLP320=

METAR CYSB 251400Z 15010KT 20SM BKN027 M01/M02 A3042 RMK SC7 CU 
ASOCTD SLP322=

TAF CYSB 251338Z 2514/2602 16012KT P6SM BKN040 PROB30 2514/2516 
BKN006 
BECMG 2516/2518 18015G25KT 
FM252000 18015G30KT P6SM SCT040 BKN140 
RMK NXT FCST BY 252000Z=

## KITCHENER/WATERLOO/ON

METAR CYKF 261600Z AUTO 19013G20KT 9SM BKN069 BKN080 BKN085 OVC110 
10/04 A3044 RMK SLP316=

SPECI CYKF 261527Z AUTO 19014G24KT 9SM BKN069 BKN083 OVC085 09/03 
A3045 RMK SLP320=

METAR CYKF 261500Z AUTO 20015G20KT 9SM -RA SCT025 BKN063 OVC080 09/03 
A3046 RMK SLP322=

SPECI CYKF 261456Z AUTO 20014G20KT 9SM -RA SCT027 BKN063 OVC080 09/03 
A3046 RMK SLP323=

METAR CYKF 261400Z AUTO 19011G16KT 9SM BKN027 BKN056 BKN075 OVC099 
08/03 A3045 RMK SLP321=

TAF CYKF 261338Z 2614/2702 20015G25KT P6SM BKN065 OVC080 TEMPO 
2614/2702 P6SM -SHRA BKN020 
RMK FCST BASED ON AUTO OBS. NXT FCST BY 262000Z=

# Text boxes

Rubric – Total 17 points

- Complete a navigation log for the above flight.

  - Complete the pre-flight planning portion only

  - Do not complete the in-flight log or checkpoints

  - Complete all calculations for VFR minimum requirements only

- Answer the 16 questions plus the bonus question.

| Navigation Log | 0 points Navigation log not submitted | 1 Point Navigation log submitted |
| --- | --- | --- |
| Questions | 16 Points 1 point per question Bonus question worth 1 point |